This instruction is for Eunhasu upgrade which is not able to upgrade by clicking the upgrade button on the Eunhasu upgrade page.
There are 3 ways to do the upgrade.
First, Samba : It is for Windows file sharing protocol. To access sMS-200 through SMB, type \\eunhasu\mwdata\music in windows file explorer. The sMS-200 should be connected in the same network.
Second, USB memory stick : It is internal debug mode. To use this method for the upgrade, several conditions should be matched.
Finally, imageUSB utility : This is external application to write entire image of the latest version to SD card.
# By samba share
1. Download upgrade-last.tar file from server
  1. sMS-200
2. Copy upgrade-last.tar to Eunhasu samba directory \\eunhasu\mwdata\music
3. Eunhasu page will be loaded like http://eunhasu/upgrade.php?upgrade_server=eunhasu/music&force=1
  1. upgrade_server={EUNHASU_IP}/music is possible
# By USB
1. Format USB to FAT32
2. Change USB label to SOTMDEBUG and it must be upper case
3. Download upgrade-last.tar file from server
  1. sMS-200
4. Copy the downloaded upgrade-last.tar to the USB root directory
5. Make file named run_debug.txt in the USB
6. run_debug.txt file must contain following strings
upgrade force
1. Remove whole inserted USB stick on sMS-200
2. Insert SOTMDEBUG USB to sMS-200
3. On working, blink the left LED
4. After finishing, device shows the left LED off
# By external utility
sMS-200 - Refer Here