# sMS-200ultra

sMS-200 is a new generation of mini network player.
- Description
- Eunhasu usage
# Exterior

The lamp illuminates when the unit is powered ON and blinks according to its operational status. Press the LED bar to turn on or off sMS-200ultra

1. Power input jack : Connect to a power supply.
2. High-End audio grade USB port : Connect to USB audio device.
3. USB 2.0 port : Connect to USB storage device.
4. microSD card connector : The micro SD card which the product OS is loaded on is inserted.
  1. Caution: do not pull out the micro SD card while the unit is powered on. Product might be damaged.
5. LAN port : Connect to a router by network cable.
6. Reset switch : Press more than 3 seconds and release the reset switch, then Eunhasu Software settings will be initialized.